## Slide 1: Economic and environmental evaluation of parallel revenue streams for hybrid energy storage systems
16.10.2024
Project update (Nov 2024)
Nicolas Seemann-Ricard

## Slide 2: Agenda
Refining research question and goals
Structure and progress
Preliminary results

## Slide 3: Refining scope and objectives
Current literature:
  High sensitivity to quickly changing parameters (market products, CAPEX)
  Many case studies, most with outdated market structure → abstraction of products
Objectives:
  Investigate the impact of participating in different electricity markets with HESS (revenue stacking)
  Investigate different system configurations: PV vs. PV + BESS vs. PV + HESS
  Evaluation based on profit-maximization and profit-CO2 multiobjective optimization
  Evaluate impact of market indicators on performance/profitability/CO2

## Slide 4: Structure and progress
Done
  Most of the data is clean and imported
  Scalable HESS modelling with cycling and calendar degradation costs but without CO2 emissions
  Preliminary analysis market data
Next tasks
  Wrap up literature review
  Settle on technological parameters and grid fees
  Implement CO2 accounting
  Implement stochasticity for aFRR activation

## Slide 5: Proof of concept
Battery SOC over 48h
Linearized degradation function (psi vs SOC)

## Slide 6: Correlating results with market metrics: mean prices and price volatility

## Slide 9: This week:
Lit!

## Slide 10: This week:
Energy activation modelling
Case studies
Update for McKenna
  Markets, model, results, next steps

## Slide 11: Refining research question and goal
Investigate the impact of participating in different electricity markets with HESS (revenue stacking), including uncertainty of activation and regulatory constraints, under varying market conditions
  Day-ahead and intraday wholesale (DA, ID)
  Primary control reserve (PCR)
  Secondary control (aFRR)
  Peak shaving
Investigate different system configurations: PV vs. PV + BESS vs. PV + HESS
Evaluation based on profit-maximization and profit-CO2 multiobjective optimization
Case study for German industrial plants with PV production.
Detailed degradation modelling ex-post

## Slide 12: Problem formulation: market and technology mixes
Technology mixes:
  PV only,
  PV + BESS,
  PV + BESS + supercap + (thermal storage)
Markets:
  Peak shaving (PS)
  PS + DA & ID
  PS + DA & ID + PCR & aFRR
Industrial load
PV
Grid
BESS
Supercap
Thermal storage

## Slide 13: Problem formulation: system operation
Degradation
SOC
SOC
SOC
Supercap
Thermal storage
Battery
FCR (30min)
FCR (30min)
aFRR up (1h)
aFRR down (1h)
SOC
Arbitrage and peak shaving
Wholesale markets (Day-ahead, intraday)
Peak shaving
PV production
Capacity markets (FCR, aFRR)
Aggregated capacity

## Slide 14
Today
Notes: AND 15min day ahead starting next year

## Slide 15: Analysis and modelling of varying market conditions
Characterize market months (market rules, average prices, volatility)
Pair with PV production, local load, carbon intensity
 Will allow to analyse potential revenues under specific market conditions to make predictions about future trends
Industrial loads

## Slide 16: Optimization problem: main features
Operational objective function:
Constraints:
  Flow, technical
  Regulatory constraints of markets (e.g. volume ticks, minimum SOC)
Solving will heavily depend on problem complexity once implemented
Single-stage (month-long) with variable storage capacities might be too complex
  Possibly implement a two-stage optimization:
    1st stage on shorter timescales builds a surrogate model for system configuration
    2nd stage solves for longer timescales
Optimization problem: solving

## Slide 17: Evaluation of results
System costs with different market participation (peak shaving, arbitrage, balancing services)
System costs with different systems (PV, BESS, HESS)
System costs vs market conditions and characteristics
System costs vs emissions costs
Expected lifetime (degradation) vs market conditions
NPV of the system

## Slide 18: Project planning
Today
Market data analysis